## Slide 1
The Solar Resource
Chapter 4

## Slide 2: The solar resource
Solar energy is radiant light and heat from the Sun that is harnessed using a range of ever-evolving technologies such as solar heating, photovoltaics, solar thermal energy, solar architecture, molten salt power plants and artificial photosynthesis.

## Slide 3: The solar resource
About 4 billion kilograms of mass per second are converted into energy as described by Einstein’s famous relationship . This fusion has been continuing reliably for the past 4 or 5 billion years and is expected to continue for another 4 or 5 billion years.
To design and analyze solar systems that will convert some of that sunlight into electricity, we need to work our way through a fairly straightforward, though complicated looking, set of equations to predict where the sun is in the sky at any time of day as well as its intensity.

## Slide 4: The solar resource
The Earth receives 174 petawatts (PW) of incoming solar radiation (insolation) at the upper atmosphere. Approximately 30% is reflected back to space while the rest is absorbed by clouds, oceans and land masses

## Slide 5: The solar resource
Solar power is the conversion of sunlight into electricity, either directly using photovoltaics (PV), or indirectly using concentrated solar power (CSP).
In the last two decades, photovoltaics (PV), also known as solar PV, has evolved from a pure niche market of small scale applications towards becoming a mainstream electricity source.
A solar cell is a device that converts light directly into electricity using the photoelectric effect.

## Slide 6: Worldwide PV Installation

## Slide 7: Worldwide PV Installation
Source:
https://en.wikipedia.org/wiki/
Growth_of_photovoltaics

## Slide 8: The solar spectrum
A blackbody is defined to be a perfect emitter as well as a perfect absorber.
The wavelengths emitted by a blackbody depend on its temperature as described by Planck’s law:

## Slide 9: The solar spectrum
The area under Planck’s curve between any two wavelengths is the power emitted between those wavelengths, so the total area under the curve is the total radiant power emitted. That total is conveniently expressed by the Stefan–Boltzmann law of radiation:

## Slide 10: The solar spectrum
Wien’s displacement rule tells us the wavelength at which the spectrum reaches its maximum point:

## Slide 11: Electromagnetic Spectrum
Source: en.wikipedia.org/wiki/Electromagnetic_radiation
Visible light has a wavelength of between 0.4 and 0.7 μm, with ultraviolet values immediately shorter, and infrared immediately longer

## Slide 12: Earth receives Sunlight and reflects Earthlight
The Earth’s atmosphere reacts very differently to the much longer wavelengths emitted by the Earth’s surface compared with the relatively shorter wavelengths arriving from the Sun.

## Slide 13: Irradiance
A solar radiation makes its way toward the earth’s surface, some of it is absorbed by various constituents in the atmosphere, giving the terrestrial spectrum an irregular, bumpy shape.
The terrestrial spectrum also depends on how much atmosphere the radiation has to pass through to reach the earth surface.
If a point source radiates light uniformly in all directions and there is no absorption, then the irradiance drops off in proportion to the distance from the object squared, since the total power is constant and it is spread over an area that increases with the square of the distance from the source.

## Slide 14: Air Mass Ratio
Air mass ratio: the length of the path h2 taken by the sun’s rays as they pass through the atmosphere, divided by the minimum possible path length h1, which occurs when the sun is directly overhead (solar noon):
h1
h2
beta: the altitude angle of the sun
beta
h2
h1
horizon
“top” of atmosphere

## Slide 15: The earth’s orbit
The earth revolves around the sun in an elliptical orbit, making one revolution every 365.25 days.
The earth sweeps out what is called the ecliptic plane
Earth’s spin axis is currently 23.45˚
Equinox – equal day and night, on Mar. 21 and Sep. 21
Winter solstice – North Pole is tilted furthest from the sun
Summer solstice – North Pole is tilted closest to the sun

## Slide 16: The earth’s orbit
152 Mkm
147 Mkm
The tilt of the Earth’s spin axis with respect to the ecliptic plane (red) causes seasons

## Slide 17: The earth’s orbit
This variation in distance is described by the following relationship
where n is the day number,

## Slide 18: Altitude angle of the sun at solar noon
In many situations, it is quite useful to be able to predict exactly where in the sky the sun will be at any time, at any location, on any day of the year.
Knowing that information we can, for example, design an overhang to allow the sun to come through a window to help heat a house in the winter while blocking the sun in the summer.

## Slide 19: Altitude angle of the sun at solar noon
The angle formed between the plane of the equator and a line drawn from the center of the sun to the center of the earth is called the solar declination.

## Slide 20: Altitude angle of the sun at solar noon
Exact values of declination, which vary slightly from year to year, can be found in the annual publication The American Ephemeris and Nautical Almanac.
The declination can be computed by the following function:
where: day number n= 1(Jan1), 32 (Feb1), 60(Mar1),…etc.

## Slide 21: Altitude angle of the sun at solar noon
during the summer solstice, all of the earth’s surface above latitude 66.55◦ N (90–23.45◦) basks in 24 h of daylight, while in the southern hemisphere below latitude 66.55◦ S it is continuously dark. Those latitudes, of course, correspond to the Arctic and Antarctic Circles.

## Slide 22: Altitude angle of the sun at solar noon
Solar noon – sun is directly over the local line of longitude
Rule of thumb for the Northern Hemisphere - a south facing collector tilted at an angle equal to the local latitude.
During solar noon, the sun’s rays are perpendicular to the collector face

## Slide 23: Altitude angle of the sun at solar noon
The altitude angle is the angle between the sun and the local horizon directly beneath the sun.
Solar Rays

## Slide 24: Best tilt angle for PV module for the greatest insolation
Maximum annual solar collector performance at two equinox days:
  Achieved when collector is facing equator (south), with a tilt angle equal to latitude (assume northern hemisphere)
Why?
  In this geometry (the collector facing the equator with this tilt angle) the solar radiation it receives will be normal to its surface at the two equinoxes

## Slide 25: Maximum Performance on Any Day
Maximum solar performance:
  Achieved when collector is facing equator, with a tilt angle equal to 90o - N
What is N ? Altitude angle: angle between the sun and the local horizon (this is a plane, not a line!) directly beneath the sun at solar noon:
So, for best performance, we need to adjust tilt of PV module:
(This still needs to be adjusted according to solar position; more later)

## Slide 26: Solar position at any time of day
The location of the sun at any time of the day can be described in terms of its altitude angle β and its azimuth angle
Azimuth Angle
Altitude Angle

## Slide 27: Solar position at any time of day
Azimuth is an angular measurement in a spherical coordinate system. It is defined by the angle between the projected vector and a reference vector on the reference plane, where projected vector is the vector from an observer (origin) to a point of interest and the reference vector usually points to north.

## Slide 28: Solar position at any time of day
The following two equations allow us to compute the altitude and azimuth angles of the sun.
where: =altitude, S= azimuth, L=latitude,  =declination, H=hour angle
Note: In spring & summer in early morning and late afternoon azimuth may be greater than 90o, so must be tested

## Slide 29: Solar position at any time of day
meridian: at any instant, the sun is directly over a particular line of longitude, called the sun’s meridian. The difference between the local meridian and the sun’s meridian is the hour angle, with positive values occurring in the morning before the sun crosses the local meridian.

## Slide 30: Solar Hour angle (H)
Solar Hour angle (H) is the number of degrees the earth must rotate before the sun will be directly above your local meridian (local line of longitude, due ‘true’ south for most of us).
Note: In spring & summer, in the early morning and in the late afternoon azimuth may be greater than 90o, so azimuth angle must be tested

## Slide 31: Solar position at any time of day
Solar altitude and azimuth angles for a given latitude can be conveniently portrayed in graphical form.

## Slide 32: Sun Path Diagrams for Shading Analysis
Now we know how to locate the sun in the sky at any time; this is useful for perfect tracking of the solar rays
This can also help determine what sites will be in the shade at any time
Sketch the azimuth and altitude angles of trees, buildings, and other obstructions
Sections of the sun path diagram that are covered indicate times when the site will be in the shade

## Slide 33: Maximize your Solar Window

## Slide 34: Sun Path Diagrams for Shading Analysis
Superposition of obstructions: tying the plumb-bob onto the protractor so that when you sight along the top edge of the protractor the plumb-bob hangs down and provides the altitude angle of the top of the obstruction.

## Slide 35: Sun Path Diagrams for Shading Analysis
The site is a proposed solar house with a couple of trees to the southeast and a small building to the southwest. In this example, the site receives full sun all day long from February through October. From November through January, about one hour’s worth of sun is lost from around 8:30 a.m. to 9:30 a.m., and the small building shades the site after about 3 o’clock in the afternoon.

## Slide 36: Sun Path Diagrams for Shading Analysis
The following table shows an example of the hour-by-hour insolations available on a clear day in January at 40◦ latitude for south-facing collectors with fixed tilt angle, or for collectors mounted on 1-axis or 2-axis tracking systems.

## Slide 37: California Solar Shade Control Act
The shading of solar collectors has been an area of legal and legislative concern (e.g., a neighbor’s tree is blocking a solar panel)
California has the Solar Shade Control Act (1979) to address this issue
  No new trees and shrubs can be placed on neighboring property that would cast a shadow greater than 10 percent of a collector absorption area between the hours of 10 am and 2 pm.
  Exceptions are made if the tree is on designated timberland, or the tree provides passive cooling with net energy savings exceeding that of the shaded collector
  First people were convicted in 2008 because of their redwoods

## Slide 38: The Guilty Trees were Subject to Court Ordered Pruning
Source: NYTimes, 4/7/08

## Slide 39: Shading Analysis Using Shadow Diagrams
The start of a shadow diagram for a particular day of the year at a particular location

## Slide 40: Shadow Diagram
By mapping out those shadow lines, month-by-month, a shadow diagram can be generated for any given latitude.
A Shadow diagram drawn for 40̊ N latitude. Curves are drawn for the 21st of each month.

## Slide 41: Example 4.5 Spacing For Rows of Collectors
Long rows of solar collectors lined up along an east-west direction are located in a spot at 40̊ N latitude. The backs of the solar racks are 2 ft high.
Use the shadow diagram in Figure 4.16 to decide how far apart the rows should be placed to assure no shading from one row to another anytime between 9:00 A.M. and 3:00 P.M.
Using Equation 4.8 and 4.9, what would the spacing be to avoid shading between 8:00 A.M. and 4:00 P.M.?

## Slide 42: Example 4.5
Solution
a. Imagine a 2-ft-high peg at the back edge of a row of collectors as shown above. Clearly, the worst day, with the longest north-south shadows is the winter solstice, December 21st. From Figure 4.16 the longest shadow toward the north at 9:00 A.M. or 3:00 P.M. is close to three pegs long (3 squares back). With each peg being 2 ft high, the separation distance should be about
b. From Equation 4.8, using the solstice declination of and an hour angle H = 60̊ (4 h before solar noon):
So, from Figure 4.15, the length of the shadow at that time is

## Slide 43: Example 4.5
From Equation 4.9, the azimuth angle of the shadow is
Since it is winter, we do not need to check to see if the azimuth is greater than 90̊. The north-south distance behind the 2 ft back of the modules is
We could have gotten this answer much more easily by just counting squares in the shadow diagram. Also note that spacing has gone from 6 ft to over 12 ft just to capture a modest amount of early morning and late afternoon sunlight (one more hour) during just a couple of winter months.

## Slide 44: Solar time and civil (clock) time
For most solar work, it is common to deal exclusively in solar time (ST), where everything is measured relative to solar noon (when the sun is on our line of longitude).
Time zones around the world are expressed as positive or negative offsets from what used to be called Greenwich Mean Time (GMT), but what is now more precisely defined as Coordinated Universal Time (UTC).

## Slide 45: Solar time and civil (clock) time
As the earth moves through its orbit, the difference between a 24-h day and a solar day changes following an expression known as the equation of time, E:
Where
Putting together the longitude correction and the equation of time gives us the final relationship between local standard clock time and solar time.

## Slide 46: Solar time and civil (clock) time
The Equation of Time adjusts for the earth’s tilt angle and noncircular orbit.

## Slide 47: Sunrise and sunset
A sun path diagram can be used to locate the azimuth angles and approximate times of sunrise and sunset.
At sunrise and sunset, the altitude angle β is zero so we can write
Solving for the hour angle at sunrise, , gives
Since the earth rotates 15◦/h, the hour angle can be converted to time of sunrise or sunset using

## Slide 48: CLEAR SKY DIRECT-BEAM RADIATION

## Slide 49: Total Solar Flux
Direct Beam
  Radiation that passes in a straight line through the atmosphere to the solar receiver (required by solar concentrator systems)
Diffuse
  Radiation that has been scattered by molecules and aerosols in the atmosphere
Reflected
  Radiation bouncing off ground or other surfaces

## Slide 50: Total Solar Flux (units)
Other units involving British Thermal Units, kilocalories, and langleys may also be encountered. Conversion factors between these units are given in Table:
Conversion Factors for Various Insolation Units

## Slide 51: The extraterrestrial solar flux.
The starting point for a clear-sky radiation calculation is with an estimate of the extraterrestrial (ET) solar insolation, , that passes perpendicularly through an imaginary surface just outside of the earth’s atmosphere

## Slide 52: The extraterrestrial solar flux
I_B = A exp (-km)

## Slide 53: Flux changes based on module orientation
Fixed Panel facing south at 40o N latitude
  40o tilt angle: 2410 kWh/m2
  20o tilt angle: 2352 kWh/m2 (2.4% loss)
  60o tilt angle: 2208 kWh/m2 (8.4% loss)
Fixed panel facing SE or SW (azimuth)
  40o tilt angle: 2216 kWh/m2 (8.0% loss)
  20o tilt angle: 2231 kWh/m2 (7.4% loss)
  60o tilt angle: 1997 kWh/m2 (17.1% loss)

## Slide 54: Total Clear Sky Insolation on a Collecting Surface
Direct-Beam Radiation
The incidence angle θ between a normal to the collector face and the incoming solar beam radiation

## Slide 55: Total Clear Sky Insolation on a Collecting Surface
Diffuse Radiation
The diffuse insolation on a horizontal surface IDH is proportional to the direct beam radiation IB no matter where in the sky the sun happens to be:
Diffuse radiation can be scattered by atmospheric particles and moisture or reflected from clouds.
where C is a sky diffuse factor
Diffuse radiation on a collector assumed to be proportional to the fraction of the sky that the collector

## Slide 56: Total Clear Sky Insolation on a Collecting Surface
The ground is assumed to reflect radiation with equal intensity in all directions.
The fraction of that ground-reflected energy that will be intercepted by the collector depends on the slope of the panel

## Slide 57: Tracking Systems
Most residential solar systems have a fixed mount, but sometimes tracking systems are cost effective
Tracking systems are either single axis (usually with a rotating polar mount [parallel to earth’s axis of rotation), or two axis (horizontal [altitude, up-down] and vertical [azimuth, east-west]
Ballpark figures for tracking system benefits are about 20% more for a single axis, and 25 to 30% more for a two axis

## Slide 58: Benefits of tracking
Two axis tracking – track the sun both in azimuth and altitude angles
  3,305 kWh/m2
  37.1% improvement at 40o N latitude
Single axis – tracks only one angle or the other; if the tilt angle equals local latitude (called polar mount), rotates about its axis at the same rate as the earth turns, 15 deg/h, then the centerline of the collector will always face directly into the sun. The incidence angle of the sun’s rays will be equal to the solar declination angle.
  3,167 kWh/m2
  31.4% improvement at 40o N latitude

## Slide 59: Tracking Systems
Two-Axis Tracking
Two-axis tracking angular relationships

## Slide 60: Tracking Systems
Two-Axis Tracking
A single-axis tracking mount with east–west tracking. A polar mount has the axis of rotation facing south and tilted at an angle equal to the latitude
Single-Axis Tracking

## Slide 61: Tracking Systems
Two-Axis Tracking
The effective tilt, which is the angle between a normal to the collector and the horizontal plane, is given by:

## Slide 62: Tracking Systems
Four ways to do single-axis tracking for solar collectors
Two approaches rotate the collectors along a horizontal axis, with either a north–south or an east–west orientation. The other two have a fixed tilt angle; one rotates about a vertical axis and the other about a tilted axis.

## Slide 63: Monthly and Annual Insolation
annual performance is relatively insensitive to wide variations in collector orientation for nontracking systems.

## Slide 64: Monthly and Annual Insolation
For a fixed system the total annual output is somewhat insensitive to the tilt angle, but there is a substantial variation in when the most energy is generated

## Slide 65: Solar radiation measurements
Creation of solar energy databases began in earnest in the United States in the 1970s by the National Oceanic and Atmospheric Administration (NOAA) and later by the National Renewable Energy Laboratory (NREL).

## Slide 66: Solar radiation measurements
A map of the solar measurement stations is shown in Figure:

## Slide 67: Solar radiation measurements
By temporarily affixing a shade ring to block the direct beam, a pyranometer can be used to measure just diffuse radiation

## Slide 68: Solar radiation measurements
The most accurate of these incorporate a sensor surface that consists of alternating black and white segments

## Slide 69: US Annual Insolation

## Slide 70: Worldwide Annual Insolation
TOTAL INSTALLED PV capacity: In 2007 worldwide PV peak was about 7800 MW, with almost half (3860 MW) in Germany, 1919 MW in Japan, 830 MW in USA and 655 MW in Spain

## Slide 71: Solar insolation under normal skies
Of greater importance is estimating the radiation that will be seen on a collector under more realistic conditions.
The NSRDB provides the starting point for creation of what is called a typical meteorological year (TMY) database of location-specific hour-by-hour insolation and weather data.

## Slide 72: Solar insolation under normal skies
We can convert terrestrial DNI and DHI data into hourly irradiation onto any of the tracking or fixed-orientation solar collector with the following equations:

## Slide 73: Average monthly insolation
Historically, most of the long-term collected site-specific data have been insolation measured on a horizontal surface.
One approach to convert these older data into expected radiation on a tilted surface depends on sorting out what portion of the total measured horizontal insolation is diffuse and what portion is direct beam, .

## Slide 74: Average monthly insolation
Radiation data for Boulder are plotted below:

## Slide 75
End